## Slide 1: Force Scaling in Rehab
Physical Human Robot Interaction
Thorbjörn Höllwarth, Michel Vogt
Supervisor: Nadine Dominik
19th of December 2024, ETH Zürich
Rehabilitation Engineering

## Slide 2: Introduction
ROBERT [1]
Notes: Robotic therapy aids recovery in stroke patients and supplements physiotherapy.
Manipulating visual feedback about performed work can help subjects break self-imposed limits in physical therapy.
This study had two parts with 4 subjects:
  Determine the just-noticeable-difference (JND) in force using a haptic paddle.
  Assess how visual distortion influences perceived effort.

## Slide 3: Methods – Setup I
Haptic Paddle
  With markings at ceratin angles for experiment 2
Integrated strain gauge
Screw engine
Rod to connect motor forces to the paddle
LabView

## Slide 4: Methods – Setup II
Characterisation
  Force sensor transfer function
    Measure gauge voltage using known weights
  Desired force transfer function
    Measure force across multiple motor voltages
Notes: Haptic paddle used with an integrated strain gauge to apply controlled forces.
Characterization steps:
  Measure the transfer function of the strain gauge.
  Calibrate the motor force applied to the paddle handle.
LabVIEW + DAQ were used for signal control and data acquisition.
Subjects: 4 participants, aged 20-25 years, with no hand impairments.

## Slide 5: Methods – Exp. 1: Just-Noticable-Difference Determination
Subject
  Place elbow on the table
  Position right hand index finger in paddle hole
  Keep the hand as steady as possible
Workflow
  Apply a reference force of 2 Newtons
  Add and subtract a delta force pair to/from the reference force for 2 seconds
  Return to the reference force
  60 trials per subject
Evaluation
  After each delta pair, ask: "Was force 1 stronger, force 2 stronger, or no difference?"
Delta Force Pair | Deviation | Strong Signal | Weak Signal
D1 | 0.25 N | 2.125 N | 1.875 N
D2 | 0.35 N | 2.175 N | 1.825 N
D3 | 0.45 N | 2.225 N | 1.775 N
D4 | 0.55 N | 2.275 N | 1.725 N
D5 | 0.65 N | 2.325 N | 1.675 N
D6 | 0.75 N | 2.375 N | 1.625 N
FPaddle
Notes: Aim: Determine the smallest force difference a subject can perceive.
Subjects used their index finger for consistency and comparability with literature.
Experiment setup:
  Subjects hooked their index finger into the paddle loop and kept it still.
  100 trials: Two forces applied for 2 seconds each, in random order.
  Subjects answered if the forces were the same or identified the higher force.
Forces were symmetrically applied around a 2 N reference force (values shown on slide).
Paddle held at zero position, and no feedback was given to avoid biases.
Explain JND
Random
Allgemeint subject fragen

## Slide 6: Methods – Exp. 2: Force Distortion
Subject
  Place elbow on the table
  Position right hand index finger in paddle hole
  Keep the hand as steady as possible
  Only flex the index finger
Workflow
  Start at zero-position
  For each distortion level:
    Tell subject to flex their finger, until the paddle has reached position [1, 2, 3, 4]
    Hold each angle for 5 seconds, return to 0-position inbetween
    64 trials per subject
Evaluation
  After each return, ask: “How would you rate your effort at this mark? [1 = minimum effort, 10 = maximum effort]”
  Effort = energy usage, exertion, fatigue
Distortion Level | Force at 6.5° | Force at 13° | Force at 19.5° | Force at 26°
0% | 1.50 N | 2.00 N | 2.50 N | 3.00 N
7% | 1.61 N | 2.14 N | 2.68 N | 3.21 N
15% | 1.73 N | 2.30 N | 2.88 N | 3.45 N
22% | 1.83 N | 2.44 N | 3.05 N | 3.66 N
FPaddle(Pos)
αposition
Notes: Aim: Determine if visual feedback influences perceived effort.
A virtual spring applied controlled forces at specific angles of the paddle (values shown on slide).
Experiment setup:
  60 trials: Subjects flexed their index finger to a target angle and held it for 5 seconds against the applied force.
  Subjects rated perceived effort on a scale of 1 to 10.
Spring constant manipulation:
  First 12 trials: Constant spring constant (baseline).
  After that: Every second trial increased spring constant by 7%, 15%, or 22% without informing the subjects.
  This design controlled for muscle fatigue vs. intentional force distortion.
Force Distortion Introduction:
…
Effort definition

## Slide 7: Results - JND
 | Δ Force (%)
Ratio 50% | 19.17%
Ratio 75% | 30.25%
JND | 11.03%

## Slide 8: Results - JND
JND | 10.78 ± 5.95 %

## Slide 9: Results – Force Distortion

## Slide 10: Results – Force Distortion

## Slide 11: Comparison To Literature
JND | Our Study | Brewer et al. (2005) [2]
Mean | 10.78 ± 5.95 % | 19.70 ± 1.85 %
Min | 6.00% | 12.06%
Max | 19.08% | 31.7%
Why the difference?
Definition of JND
Dynamic vs static
Age of subjects
JND of Index Finger

## Slide 12: Comparison To Literature
Brewer et al. (2005) [2]

## Slide 13: Limitations
# of subjects
# of trials
Controlled variables
  Finger position
  Support by other muscle groups
  Time spent at force
  Paddle position
  Muscle fatigue
  Response bias
JND | 10.78 ± 5.95 %

## Slide 14: Conclusion / Outlook
Key message:
Feedback distortion can be valuable tool in rehabilition
Future work:
Long term studies, bigger muscle groups, subject in rehab

## Slide 15: References
[1] unitedrobotics.group
[2] Brewer et al., IEEE transactions on neural systems and rehabilitation engineering (2024)